## Slide 1
The DESI Fiber View Camera
and Fiber Plane Fiducials
1
C Baltay
March 26, 2015

## Slide 2: Fiber View Camera Key Personnel
A collaborative effort between LBNL and Yale University
  C. Baltay, W. Emmet, N. Padmanabhan, B. Horowitz, Terry Girard*, Dana Cassetti*, Yale
  R. Besuner, M. Lampton, and J. Silber, LBNL
  *members of Prof. Bill Van Altena’s precision astrometry group at Yale

## Slide 3: The Function of the Fiber View Camera
5000 fibers on the fiber plane will be positioned to their desired positions by a computer controlled mechanism. The expected initial precision of the fiber positioners is expected to be 20 microns rms, 50 microns max. Fibers will be positioned to a 5 μm RMS accuracy using the Fiber View Camera.
The Fiber View Camera is designed to take an image of the fiber plane to measure the position of each fiber with a 3 μm RMS accuracy after the mechanism is done positioning them.
The positions of misplaced fibers can then be corrected based on the information from the Fiber View Camera.
Estimate is that one or two iterations will get fibers in the right positions

## Slide 4: The DESI Fiber View Camera
Design
Prototype test results
Support Structure
Illuminated Fiducials

## Slide 5: Location of the Fiber View Camera
Fiber Plane
Spectrometer Enclosure
LED
Fibers
Fiber View Camera
Corrector Optics
Primary Mirror
12.25 m

## Slide 6: Fiber View Camera Requirements
Feature Requirement Present
CDR p. 123 Performance
Absolute Position Meas. 3 μm RMS 2.5 μm RMS
Nearest Neighbor Dist. < 1 mm 0.7 mm
Exposure Time < 2 sec 1 sec
Readout Time < 2 sec 5 sec*
Computing Time 1 sec < 1 sec
* Limited by USB cable between camera and computer,
will be 1 sec with ethernet cable and modified
readout electronics

## Slide 7: Some Design considerations
Input dimensions
  Fiberplane diameter is order of 830 mm
  CCD size ~37 mm
  Fiberplane to camera L = 12,250 mm
Demagnification desired ~ 25
Demag ~ f/L
Camera focal length f ~ 600 mm
At a demagnification of 25, a 5 micron precision on the fiber plane translates to 0.2 microns on CCD, or 1/30 of a 6 micron pixel (33 millipixels)
A bit of history-Nov 2013 had the FVC obove the primary mirror, 8.9 meters from fiber plane with a 400 mm lens

## Slide 8
Fiber View Camera Design Specifications
CCD Kodak KAF-50100
Pixel Count 50 Mpix
Pixel Array 6132x8176
Pixel Size 6 µ x 6µ
Active Area 37mm x 49 mm
Quantum Efficiency 25%
Dark Current at 250C 15 e/pix/sec
Read Noise 12.5 e
Read Out Time 1 sec
Lens Canon EF600mm f/4 L II USM
Focal length 600 mm
Aperture 150 mm
Demagnification 25
Electronics FLI Proline PL50100
Readout time 1 sec
Focusing, aperture Computer controlled

## Slide 9: Effects of the Corrector Optics
Ran beam traces using BEAM4 program, simulating images of the fiberplane through the corrector
Used the current baseline design of the corrector optics as input (E22, DESI-DOC-329)
Specifications for Canon and Nikon lenses not available. Found the specs for a 52 mm Tessar lens,
scaled it to 600 mm focal length
Obtained acceptable images with this corrector and lens!!

## Slide 10: Ray Traces to the Fiber View Camera
Fiber Plane
Corrector Optics
Fiber View Camera

## Slide 11: Corrector Optics
Curved Fiber Plane
Curved Fiber Plane

## Slide 12: The Fiber View Camera
Using BEAM4 Ray tracing program to design and check optics
600 mm Tessar Lens
Kodak 6K x 8K CCD

## Slide 13: Results of the Ray Traces
R on Fiber Plane | r on CCD | Image Full Size on CCD*
mm | mm | microns
0 | 0.0 | 3.4
100 | -4.133 | 4.6
200 | -8.552 | 4.0
300 | -12.648 | 5.0
415 | -17.098 | 5.5
* Including fiber size, not including diffraction

## Slide 14: Radial Linearity
R is the distance from the center of the CCD in mm
Distance from Center on Fiber Plane (mm)
R (mm)

## Slide 15: Radial Distortion
Distance from Center on Fiber Plane (mm)
Deviation from Linear (mm)

## Slide 16: In Situ Calibration
It will be important to calibrate the camera during the operation of the survey with each exposure using fixed fiducial fibers on the focal plane.
Plan on using 100 fixed fiducial fibers
Calibration uses 3rd order polynomial
  X = a1+a2x+a3y+a4xy+a5x2+a6y2+a7x3+a8y3+a9x2y+a10xy2
  Y = b1+b2x+….
Will need precision measurements of the fiducial fiber positions before installation of the fiber plane.
Also plan to have fiducials on the ten Guide/Focus/Alignment (GFA) sensors on the periphery of the focal plane which will be imaged on the Fiber View Camera

## Slide 17: Fiber View Camera R&D Plan Completed
Goal of the R&D Program was to demonstrate that the required 3 micron precision on the fiber position is achievable. To do this the plan was to:
  Design and build a prototype camera
  Design and build a test setup at Yale with a mock up of a portion of the fiber plane with fibers with precisely measured positions
  Carry out the test by imaging the mock fiber plane with the Fiber View Camera and analyzing the results

## Slide 18: CCD, electronics, and lens assembled Completed May 1, 2012 with 400 mm lens

## Slide 19: Fiber Plane Prototype 64 fibers total

## Slide 20: Precision Measuring Machine
Measured positions of the 64 fibers to a precision
of 1.5 microns to compare with the FVC images

## Slide 21: Sewer Pipe Light Baffle

## Slide 22: Centroiding Position Error on CCD
Number of Exposures
Millipixels on CCD
Xave = 13.0 millipixels
Yave = 14.3 millipixels
Each entry is an exposure with 64 fibers

## Slide 23: Centroiding Position Error on Fiber Plane
Microns on Fiber Plane
Number of Exposures
Each entry is an exposure of 64 fibers
Xave = 1.80 microns
Yave = 1.98 microns
3 micron
Goal

## Slide 24: FVC Time Sequence Goals
Activity | Time Required
Exposure time | 1 second
Camera readout | 1 second
Centroid calculation | 1 seconds
Total per Iteration | 3 seconds
Will develop the electronics, computers and
software to control the Fiber View Camera In the
context of the overall Telescope Control System.

## Slide 25: Recent Work to Speed up Processing
In Nov 2013 we used Readout program supplied by FLI with the camera, that read CCD onto a disk. A major part of the processing time was to read data from the disk, do some household chores and distribute data to the multiple processors
Terry Girard and David Rabinowitz rewrote this reading routine to read data directly into the memory of the processing computers (much more efficient)
Plus made a number of tweaks to the centroiding and position calibrating routines to make them more efficient
Were able to reduce processing time to under a second

## Slide 26: Simulation of 5000 fibers in FVC
Generated simulation of 5000 fibers on CCD using actual FVC fiber images on actual FVC exposure with actual noise and background. Each fiber was distributed randomly within area of the 5000 fiber positioners

## Slide 27: FVC Timing
Action | Goal (sec) | Present (sec) | Future (sec)
Exposure Time | 1 | 1 | 1
Readout Time | 1 | 5.6 | ~1 ?
Processing Time | 1 |  | 
Centroid finding |  |  | 
4 processors |  | (0.66) | (0.66)
8 processors |  | 0.51 | 0.51
Astro calibration |  | 0.06 | 0.06
Total time/iteration | 3 | 7.2 | < 3

## Slide 28: Exploring the Parameter Space
It looks like the prototype fiber view camera is able to provide better then the required 3μ resolution on the fiber plane. We next turned to explore the dependence on various parameters:
Parameter Optimum Value
Dependence on the number of fiducial fibers 30 or more
FWHM of the fiber image on the CCD 1.6 pixels
Light level coming out of the fibers 25,000 e/image
Depth of field, diffraction limit 1.6 pixels at f/16
The f stop of the camera lens f/16 most robust
Turbulence due to thermal gradients negligible
Effect of off-angle illumination of the fibers negligible

## Slide 29: Dependence on FWHM of image on CCD
Image FWHM on CCD (pixels)
Resolution on Fiber Plane (μ)

## Slide 30: Depth of Field at Various f stops
Focus (object distance in cm)
FWHM on CCD (pixels)
Diffraction spot size = λ x f/no =10 μ = 1.6 pixels
for monochromatic light with λ = 0.6μ and f/16

## Slide 31: Diffraction Limit vs. fstop
Parameter | f/5.6 | f/10.4 | f/16
Aperture dia d | 106 mm | 58 mm | 38 mm
δΘ = λ/d | 5.7x10-6 rad | 10.3 x 10-6 rad | 16 x 10-6 rad
f x δΘ | 3.4 μ | 6.2 μ | 9.6 μ
Image size(pixls) | 0.6 | 1.0 | 1.6
Minimum image size due to diameter of the fibers:
120μ de-magified by 25 gives 4.8μ image dia
or 0.8 pixels on CCD. We realized this early on
and said that we would have to defocus the image.
The diffraction limit at f/16 is doing this for us over
a wide range of focus positions, making f/16 very
robust. At lower f stops things get more delicate…

## Slide 32
Fiber View Camera Mounting Bracket

## Slide 33: Illuminated Fiducial Fibers on the Fiber Plane
20 Fiducials on the
GFA Guide Sensors
100 field fiducials on
the Fiber Plane

## Slide 34: Focal Plane 1/10 Petal
GFA
Guider/Focus/Alignement
Joe Silber

## Slide 35: FIF (field illuminated fiducial)
Joe Silber
Fiducial
Fiber Positioner

## Slide 36: GIF (GFA illuminated fiducial)
GIF
DRIVER / COMM BOARD FOR THE TWO GIFS
Joe Silber

## Slide 37: Two types of fiducials
FIELD ILLUMINATED FIDUCIAL (FIF)
Essentially identical size, interfaces as fiber positioner
GFA ILLUMINATED FIDUCIAL (GIF)
Same front end as FIF, but different interfaces as fiber positioner
Mates to positioner hole features
Mates to positioner electronics driver board
At focal surface
Mates to GFA shell
Joe Silber

## Slide 38: Fiducial Front end
FIF
GIF
GLUE PORT
SINGLE-MODE FIBER
(LENGTH 39.6 MM)
470 NM SMT LED
(AVAGO HSMN-C170 OR EQUIVALENT)
SMALL BOARD (SCREWED ON)
CERAMIC
FERRULE
PIGTAIL

## Slide 39: Ceramic Fiber Ferrule

## Slide 40: Illuminated Fiducial Fiber Tips
GLUE PORT
SINGLE-MODE FIBER
(LENGTH 39.6 MM)
CERAMIC
FERRULE

## Slide 41: Tip of Illuminated Fiducial
Joe Silber

## Slide 42: Backup slides

## Slide 43: CCD Choice
CCD | Array | Pixel Size | Price
Kodak KAF-50100 | 6K x 8K | 6 μ x 6 μ | 5 K$
DALSA FTF-6080M | 6K x 8K | 6 μ x 6 μ | 25 K$
BAE (Loral) CCD-595 | 9K x 9K | 9 μ x 9 μ | 55 K$
STA STA-1600A | 10K x 10K | 9 μ x 9 μ | 50-60 K$
Considered 4 Frontside Illuminated, Monochrome Sensors

## Slide 44: Lens Choice
Lens | Field of View | Resolution | Price
Canon EF 600mm f/4L USM | 6 o | 125 lines/mm | 13 K$
Canon EF 400mm f/5.6 DO IS USM | 6o | 125 lines/mm | 1.3 K$
Canon EF 400mm f/2.8 L IS II USM | 6o | Better then the f/5.6 | 11.5 K$
Schneider Apo-Tele-Xenar 400mm f/5.6 | 29o | 50 lines/mm | 2.4 K$
Rodenstock Apo-Sironar S 360mm f/6.8 | 40o | 76 lines/mm | 4.4 K$

## Slide 45: Electronics and Package Choice
Camera | CCD Used | Array/Pixels | Price *
FLI Proline PL50100 | Kodak KAF 50100 | 6K x 8K/ 6μ | 21K$
Illunis RMV-50M | Kodak KAF 50100 | 6K x 8K/ 6μ | 30K$
Spectral Instr 1100S | Kodak KAF 50100 | 6K x 8K/ 6μ | 40K$
Spectral Instr 1110S | Loral CCD 595 | 9K x 9K/ 9μ | 150K$
STA Custom Camera Mega-Vision E7 Cam Back | STA 1600A Kodak KAF 50100 | 10K x 10K/ 9μ 6K x 8K/ 6μ | 75 – 150K$ 24K$
* Prices include the CCD

## Slide 46: Focal length of FVC Lens for Proto-DESI
FVC to Focal Plane Dist | Lens Focal Length | Demag | Precision on CCD | Precision on Fiber Plane
8.9 m | 400 mm | ~21 | 0.12 μ | 2.5 μ
12.5 m | 600 mm | ~20 | 0.12 μ | 2.4 μ
12.5 m | 400 mm | ~30 | 0.12 μ | 3.6 μ
> Prototype FVC with 400 mm lens exists.
> Would prefer the 600 mm lens
for Proto DESI, as planned for
the real thing
> If money is tight, the 400 mm lens
will work fine

## Slide 47: Dependence on the Number of Fiducials
Used real data of 36 exposures with the Fiber View Camera with 64 fibers each. Selected 16 fibers as fiducials to fit the 10 coefficients in x and 10 coefficients in y in the third order polynomial transformation for each exposure. Found the resolution on the fiber plane for the remaining fibers not used as fiducials to be about 2.5 microns.
Repeated using N fibers as fiducials with N from 16 to 48. With N above 30 or so resolution of the non-fiducial fibers approached 2.0 microns, as good as we have ever seen.
With only 64 fibers the number of non fiducial fibers becomes small as N is larger( 14 for N=48) so statistics not terrific.

## Slide 48: Dependence on the Number of Fiducials
Simulated 5000 fibers on full 95 cm dia fiber plane
  Divided fiber plane into 5000 fiber areas on hex pattern
  Picked random location for each fiber in its area. These were the “TRUE” fiber center locations
  Mapped fiber positions onto CCD plane by 3rd order polynomial transformation similar to actual lens/camera transformation
  Spread fiber positions randomly by 13 millipixels on CCD (this corresponds to 1.9 microns on fiber plane)
Chose N fibers as fiducials, used these fiducials to obtain 3rd order polynomial to transform fibers to fiber plane
  X = a1+a2x+a3y+a4xy+a5x2+a6y2+a7x3+a8y3+a9x2y+a10xy2
  Y = b1+b2x+….
Compared these transformed positions to the known starting “TRUE” positions

## Slide 49: Resolution on Fiber Plane vs. no of Fiducials
Number of fiducials N
RMS on fiber plane, microns

## Slide 50: Fiber Separation Study
Center to center fiber separation (mm)
Resolution on fiber plane(μ)
Measured resolution on the fiber plane for simulated
fibers at various separations, 20 at each separation
2 μ
0.75mm x 1/25 demag=30μ on CCD
30μ on CCD=5 pixels=3 image FWHM

## Slide 51: Dependence on the Flux
Flux in image (units of 103 ADU counts)
Resolution on fiber plane (microns)
2 ADU counts = 1 electron
FWHM/√N

## Slide 52: Dependence on the Flux
There is a wide plateau between 20,000 and 80,000 ADU counts that give resolution better the 2.5μ at f/16.
With 2 ADU counts/electron this means between 10,000 and 40,000 e per image on CCD, so 25,000 is a good guess of where we should be.
Our original estimate was 75,000 e per image at f/5.6. With the smaller aperture at f/16 will still need more light out of the fibers.

## Slide 53: Possible Effect of Turbulence
Did one test to simulate turbulence in the Mayall telescope
Opened shades on windows, let the sunshine in. This heated up the sunnyside of the sewer pipe by up to 5oC
Took 20 exposures at ΔT = 1oC and at ΔT = 5oC
No significant increase in the image FWHM at f/16
f stop | Previous resolution | ΔT = 1oC | ΔT = 5oC
f/16 | 2.22 μ | 2.06 μ | 2.49 μ

## Slide 54: Fiber Illumination Input Angle
No effect on resolution on fiber plane
Illumination Angle | σ (x) microns | σ (y) microns
Sideways (4 exposures) | 2.09 | 2.35
Normal (6 exposures) | 2.11 | 2.47
Sideways (4 exposures) | 2.15 | 2.08

## Slide 55: Image Shapes at various Radii
R = 0
R = 100
R = 200
R = 300
R = 415
16
Y
X
Y
Y
Y
Y
X
X
X
X
Not including diffraction effects
-8
-8
-8
-8
-12
-12
-12
-12
-17
-17
-17

## Slide 56: Radial Image Sizes
R = 0
R =100
R = 200
R = 300
R = 415

## Slide 57: Image Sizes in Azimuth
R = 0
R = 100
R = 200
R = 300
R = 415

## Slide 58: Fiber View Camera with Proto-DESI
The beam trace simulations of the Fiber View Camera were done with the DESI corrector optics to show that good images and low radial distortion can be obtained.
For the Proto-DESI run in 2016 the DESI corrector optics will not be available. The existing Mosaic corrector optics on the Mayall 4m will be used instead.
The beam trace simulations have been repeated with the Mosaic corrector.
Acceptable image quality and low radial distortion are possible.

## Slide 59: Fiber View Camera with Proto-DESI
A focal plane with a diameter of 176.6 mm has been assumed
The Fiber View Camera location is taken to be Just below the center of the primary mirror, the same as in final DESI design.

## Slide 60
zvertex index curvature diameter
----:- ----------:----------:------------:---------:
1 : 9.10 : 1.0 : : 176 :
2 : 95.61 : 1.0 : : 231 :
3 : 124.21 : 1.4585 :-2.757328e-3 : 231 :
4 : 410.01 : 1.0 : : 280 :
5 : 423.12 : 1.5186 : : 280 :
6 : 436.62 : 1.53171 : : 280 :
7 : 446.01 : 1.0 : : 280 :
8 : 458.99 : 1.5186 : : 280 :
9 : 471.58 : 1.53171 : : 280 :
10 : 537.76 : 1.0 :-4.310902e-3 : 277 :
11 : 552.84 : 1.4585 :-1.207117e-3 : 310 :
12 : 679.98 : 1.0 :-3.585643e-3 : 349 :
13 : 719.83 : 1.4585 :-3.748688e-3 : 380 :
14 : 721.33 : 1.0 :-1.178745e-4 : 400 :
15 : 761.13 : 1.4585 :-7.247069e-4 : 420 :
16 :11546.1543 : 1.0 : 3.83734e-3 : 120 :
17 :11586.5391 : 1.7918 : 0.02730e-3 : 120 :
18 :11632.7598 : 1.0 :-2.17879e-3 : 120 :
19 :11650.0674 : 1.7039 : 4.17718e-3 : 120 :
20 :11673.1445 : 1.0 : : 37.5 :
21 :11720.0010 : 1.0 :-0.17231e-3 : 120 :
22 :11737.3086 : 1.6068 : 1.82554e-3 : 120 :
23 :11777.6934 : 1.7918 :-3.00303e-3 : 120 :
24 :12301.74162: 1.0 : : 37 :
BEAM4 Ray Trace
Fiber View Camera
with 600 mm lens
Mayall 4m Telescope
With existing Mosaic
Corrector optics

## Slide 61
Image shapes on CCD
Point source at center of
Focal plane R = 0 cm
Image sizes ~ 4 microns
(units are mm)
X final
Y

## Slide 62
Image shapes on CCD
Point source near edge of
Focal plane R = 10 cm
Image sizes ~ 4 microns
(Units are mm)

## Slide 63: Radial Linearity
R is the distance from the center of the CCD in mm
Distance from Center on Fiber Plane (mm)
R on CCD (mm)

## Slide 64: Radial Distortion
Distance from Center on Fiber Plane (mm)
Deviation from Linear (mm)

## Slide 65: Plan similar to final DESI
Image sizes of ~4 microns are too small for good centroid interpolation with 6 micron pixels. Plan to use the FVC lens at f/16 so that the diffraction limit of ~10 microns, or 1.6 pixels, gives the best centroiding precision and great stability.
The radial distortion is much smaller for Proto-DESI then for the final DESI, mostly because of the smaller focal plane diameter, so the same correction algorithm that are planned for final DESI should work fine for Proto-DESI.