## Slide 1: Supernova Surveys with WFIRST DRM1 and DRM2
C Baltay
June 1, 2012

## Slide 2: Supernova Surveys using Slitless Spectroscopy
Use Imager for SNe discovery and to get lightcurves
Use slitless spectroscopy to type supernovae and get redshifts
June 1, 2012

## Slide 3: Design Surveys for DRM 1 and DRM 2
DRM 1
1.3 m mirror
Imager with
  36 H2RG detectors
  0.18 “/pixl
  0.36 sq degrees
Filter wheel with
  4 filters
  R=75 Prism
2.5 micron λ cutoff
DRM 2
1.1 m mirror
Imager with
  14 H4RG detectors
  0.18 “/pixl
  0.56 sq degrees
Filter Wheel with
  4 filters
  R=75 Prism
2.5 micron λ cutoff
Assume 6 months for Supernova Survey

## Slide 4: Assume 4 Filter Bands
Filter | λ Central | Δ λ | λ Range
1 | 1.15 | 0.26 | 1.02 – 1.28
2 | 1.45 | 0.32 | 1.29 – 1.61
3 | 1.80 | 0.40 | 1.60 – 2.00
4 | 2.25 | 0.50 | 2.00 – 2.50
Δ λ = λ / 4.5

## Slide 5: Spectroscopy
Plan to use the slitless prism spectrometer on the filter wheel
Use resolution R=75 (150/pixel)
Limit spectra wavelength range 0.6 to 2.0μ
Each of the three synthetic filter bands will correspond to 150/4.5 = 33 pixels in the dispersion direction.

## Slide 6: Survey Cadence
Plan to run supernova survey for 1.8 years calendar time.
For DRM 2 this is for 3 microlensing periods of 6 months each (72 days on, 111 days off) + 111 days which is 658 days or 1.8 years.
Plan on supernova survey with a 5 day cadence, 33 hours per visit
(658/5)*33 hrs/24 = 180 days = 6 months

## Slide 7: Imaging/Spectroscopic Survey
Split the 33 hour visit between imaging and spectroscopy
Use the imaging to obtain the lightcurves in the three filters
Use the spectra to determine that we have a Type 1a and to get the redshift ( requires shorter exposure times compared to using spectra to get precision lightcurves)

## Slide 8: Spectroscopic Exposure Times
Use the Silicon II spectral feature at 6100Å ( FWHM=160Å, FW at base=320Å) to recognize a Type 1a and to measure redshift ( will use this for a simple estimate; ultimately will use other weaker lines as well)
Want S/N=5 (for spectra coadded from the whole sequence) for the Si feature for positive ID and
z measurement

## Slide 9: Silicon II Spectral Feature
In Observer Frame | SNe rest Frame | Z=0.5 | Z=1.0 | Z=1.5
λ central | 6100 | 9150 | 12200 | 15250
FWHM | 160 | 240 | 320 | 400
FW at base | 320 | 480 | 640 | 800
Å per pixel | 41 | 61 | 82 | 102
FWHM in pixels | 3.9 | 3.9 | 3.9 | 3.9
FW at base in pixels | 7.8 | 7.8 | 7.8 | 7.8
S/N per pixel coadded sp* | 2.1 | 2.1 | 2.1 | 2.1
S/N per pixel single sp** | 0.7 | 0.7 | 0.7 | 0.7
*Signal to noise per pixel in co-added spectra to get a S/N = 5
for the Si feature. Use 6 pixels, so 5/√6 = 2.1
**Assume that S/N in a co-added spectrum (i.e.co-add all spectra
in the lightcurve) is 3 times the S/N in a single spectrum
Conclusion: Need S/N per pixel = 0.7 for single spectra

## Slide 10: Spectroscopic Exposure times to get S/N = 0.7/pixel (1.3 m mirror))
Redshift | Exp Time(sec)
0.6 | 580
0.7 | 990
0.8 | 1800
0.9 | 2900
1.0 | 3200
1.1 | 3500
1.2 | 3900
1.3 | 4200
1.4 | 4900
1.5 | 6300
1.6 | 7700
1.7 | 9500
Ran calculations to estimate slitless spectroscopy exposure times needed to get S/N = 0.7 per pixel at various redshifts
For this calculation used Supernova fluxes from a band centered at 6100A,(the Si feature) in the supernova rest frame.
Increase times by (1.3/1.1)2 for a 1.1 m mirror
This requirement determines the maximum redshift we can go to

## Slide 11: Spectroscopic Exposure times to get S/N = 0.7/pixel (1.1 m mirror)
Redshift | Exp Time(sec)
0.6 | 810
0.7 | 1390
0.8 | 2490
0.9 | 4130
1.0 | 4550
1.1 | 4840
1.2 | 5500
1.3 | 5900
1.4 | 6780
1.5 | 8760
1.6 | 10790
1.7 | 13270
Ran calculations to estimate slitless spectroscopy exposure times needed to get S/N = 0.7 per pixel at various redshifts
For this calculation used Supernova fluxes from a band centered at 6100A,(the Si feature) in the supernova rest frame.
This requirement determines the maximum redshift we can go to with a 1.1 m mirror

## Slide 12: Survey Areas
We want square areas so we can continuously monitor it as we go around a corner every three month with a 90 degree turn of the detector plane
For DRM1 assume 36 H2RG detectors are arranged in a 6 x 6 pattern so each imager field is a square
For DRM2 arrange 14 H4RG detectors in a 7 x 2 array
  For example a pattern of 1 field long and 4 fields wide would have 7 x 8 detectors. The common square area is 7 x 7 detectors or 1.96 square degrees

## Slide 13: Nearly Square Survey Areas for DRM 2
Pattern | Detectors | Square | Area (sq deg) | No of shots
1L x 4 W | 7 x 8 | 7 x 7 | 1.96 | 4
2L x 4W | 2 x (7 x 8) | 2 x (7 x 7) | 3.92 | 8
1L x 8W | 2 x (7 x 8) | 2 x (7 x 7) | 3.92 | 8
1L x 12W | 3 x (7 x 8) | 3 x (7 x 7) | 5.88 | 12
3L x 4W | 3 x (7 x 8) | 3 x (7 x 7) | 5.88 | 12
DRM 2 has 14 H4RG detectors with 10 micron pixels
The image plane is 7 detectors Long and 2 detectors Wide
A pattern of 1L x 4W is 4 image planes arranged 1 in the L
direction and 4 in the W direction
No of shots is number of exposures to cover the area in a filter
We should stick with these patterns for best efficiency

## Slide 14: Exposure Time Calculation DRM 1
Input parameters used in the spreadsheet
  1.3 m off axis telescope
  Slitless prism spectrometer with an R = 75 (i.e.150/pixel)
  Wavelength range entering spectrometer is 0.6 to 2.0μ
  36 H2RG detectors with
    plate scale = 0.18”/pix
    read noise = 5 e
    dark current = 0.05e/pix/sec
Zodiacal light background from paper by Greg Aldering
  log10f(λ) = -17.755 – 0.73(λ – 0.61) ergs/cm2/sec/Å/arcsec2
AB magnitudes of the supernova chosen to include 80% of the supernova at each redshift

## Slide 15: Supernova Signal - counts/sec/Filter Band
The supernova signal in the three filters was calculated by transforming the observer frame filter bands to the supernova rest frame and evaluating the flux in these rest frame bands.
Z Band2 Band3 Band4
0.15 17.614 10.814 4.814
0.25 7.726 5.843 2.093
0.35 4.624 3.778 0.977
0.45 3.348 2.644 1.323
0.55 2.557 1.829 1.337
0.65 1.957 1.414 1.249
0.75 1.461 1.181 1.140
0.85 1.134 1.086 1.032
0.95 1.080 0.916 0.870
1.05 1.046 0.793 1.099
1.15 0.982 0.658 0.942
1.25 0.949 0.555 1.018
1.35 0.885 0.497 1.068
1.45 0.778 0.510 1.060
1.55 0.701 0.510 1.282
1.65 0.632 0.490 0.843
For a 1.3 m dia
unobstructed view mirror
Signals reduced by (1.1/1.3)2 for a 1.1 m mirror

## Slide 16: Imaging Exposure times
Z Band 2 Band 3 Band 4
0.15 11.5 19.4 47.5
0.25 29.1 39.6 139.5
0.35 54.8 68.4 456.7
0.45 84.4 111.4 277.3
0.55 124.2 192.9 272.9
0.65 187.2 291.8 303.8
0.75 302.3 395.7 352.6
0.85 469.8 457.8 416.0
0.95 512.5 619.8 557.1
1.05 542.5 806.3 374.3
1.15 609.1 1140.0 485.6
1.25 648.4 1575.7 425.3
1.35 736.8 1949.2 392.8
1.45 936.0 1855.3 397.4
1.55 1139.3 1850.3 291.3
1.65 1389.2 2005.4 588.6
Exposure times in each of the filter
Bands for a S/N=15 in each band
for a 1.3 m mirror
Calculated exposure times as:
t = npix [(S/N)/s]2 (Z+D+r2/t) sec
npix = no of pixels in image
S/N = 15 required signal to noise
s is SNe signal in counts/sec/band
Z is the Zodi bckgrd in cts/sec/pix
D is the dark current in cts/sec/pix
r is the read noise (assume single
read here, should change with
multiple exposures per point)

## Slide 17: Measurements Errors on each Supernova
Estimate that we need a S/N = 15 in each band to get a measurement error of 12% for each supernova
The actual exposure times we propose to use are not as long as the times we have calculated as required to get 12 % measurement error for each supernova.
Estimate actual measurement error as
σ meas = (12 %) x Sqrt (time needed for 12%/actual exp time)
Assign this error for each supernova

## Slide 18: Error Model Used
Use the program by Eric Linder to calculate Figures of Merit
Statistical errors i.e. errors that are reduced by 1/sqrt(N)
  For the intrinsic spread use σint = 0.10 + 0.33z
  measurement errors per supernova that varies with z bin
  Add these in quadrature and divide by sqrt N(z) to get σstat
Systematic ( error as suggested by Adam Riess) σsys = 0.02 [ 1.0μ/{ λ0/(1+z) } ]
where λ0 is the center of the reddest filter, 1.8μ in our case.
Add these in quadrature σtot = sqrt(σstat2 + σsys2)

## Slide 19: Supernova Intrinsic spread
Use intrinsic supernova spread as we agreed:
  Rest frame B band 16 %
  Rest frame Z band 15 %
  Rest frame J band 13 %
  Rest frame H band 12 %
For the reddest (2.0 to 2.5μ) band, this wavelength dependence translates into a z dependence, so for the calculations we use the fit σintrinsic = 0.10 + 0.033 z
This error was σintrinsic = 0.11 + 0.033 z with the reddest band at 1.6 to 2.0μ

## Slide 20: Slewing and settling time, end effects
In all of the following included the effects of
  Slewing and settling time of 40 seconds for each exposure. Added 40 sec to each actual exposure in the calculations (except when only filter change)
  End effect due to needing 35 days to follow supernova

## Slide 21: Survey Strategy for DRM 1
Z max | 1.2 | 1.4 | 1.6 | 1.7 | 
Hi z Area Imaging | 2.88 | 2.52 | 2.16 | 1.80 | 
Exp time | 1500 | 1500 | 1340 | 1500 | 
Shots/visit | 8 x 3 | 7 x 3 | 6 x 3 | 5 x 3 | 
hours/visit | 10.0 | 8.75 | 6.7 | 6.25 | 
Lo z Area Imaging | 6.48 | 6.48 | 6.48 | 6.48 | 
Exp time | 300 | 300 | 300 | 300 | 
Shots/visit | 18 x 3 | 18 x 3 | 18 x 3 | 18 x 3 | 
Hours/visit | 4.5 | 4.5 | 4.5 | 4.5 | 
Spectroscopy Hi z Exp time | 4000 | 4800 | 7700 | 9500 | 
Shots/visit | 8 | 7 | 6 | 5 | 
Hours/visit | 8.9 | 9.3 | 12.8 | 13.2 | 
Lo z Exp time | 1800 | 1800 | 1800 | 1800 | 
Shots/visit | 18 | 18 | 18 | 18 | 
Hours/visit | 9.0 | 9.0 | 9.0 | 9.0 | 

## Slide 22: 2 Tier survey to z = 1.7 DRM 1 FoM = 235
Z No S/N No S/N Total σsta σ/√N σsys σtotal
0.15 9 9.91 2 22.78 12 0.107 0.030 0.006 0.031
0.25 29 4.51 8 10.35 38 0.115 0.019 0.007 0.020
0.35 57 2.71 15 6.23 73 0.127 0.015 0.008 0.017
0.45 96 1.97 26 4.52 122 0.132 0.012 0.008 0.014
0.55 140 1.50 39 3.46 179 0.140 0.010 0.009 0.014
0.65 186 1.15 51 2.65 238 0.150 0.010 0.009 0.013
0.75 231 0.86 64 1.98 296 0.162 0.009 0.010 0.014
0.85 0 0.67 79 1.53 79 0.143 0.016 0.010 0.019
0.95 0 0.64 91 1.46 91 0.149 0.016 0.011 0.019
1.05 0 0.62 101 1.42 101 0.152 0.015 0.011 0.019
1.15 0 0.58 105 1.33 105 0.159 0.015 0.012 0.020
1.25 0 0.56 106 1.28 106 0.164 0.016 0.012 0.020
1.35 0 0.52 103 1.20 103 0.170 0.017 0.013 0.021
1.45 0 0.46 95 1.05 95 0.174 0.018 0.014 0.022
1.55 0 0.41 85 0.95 85 0.178 0.019 0.014 0.024
1.65 0 0.37 75 0.85 75 0.187 0.022 0.015 0.026

## Slide 23: Numbers of Supernovae vs z
Redshift z
No of Supernovae
Total
High z

## Slide 24: Errors on Distance Modulus vs z
magnitudes
Redshift z
Statistical errors combined with conservative
or optimistic systematic errors
Conservative
Optimistic
Statistical

## Slide 25: Errors on Supernova Distances vs. z
Redshift z
fractional error on distance
Statistical errors combined with conservative
or optimistic systematic errors
Conservative
Optimistic
Statistical

## Slide 26: Survey Strategy for DRM 2
Z max | 1.2 | 1.4 | 1.6 | 1.7 | 
Hi z Area Imaging | 3.92 | 1.96 | 1.96 | 1.96 | 
Exp time | 1000 | 1600 | 1600 | 1800 | 
Shots/visit | 8 x 3 | 4 x 3 | 4 x 3 | 4 x 3 | 
hours/visit | 6.6 | 5.3 | 5.3 | 6.0 | 
Lo z Area Imaging | 7.84 | 9.80 | 7.84 | 5.88 | 
Exp time | 300 | 350 | 350 | 400 | 
Shots/visit | 16 x 3 | 20 x 3 | 16 x 3 | 12 x 3 | 
Hours/visit | 4.0 | 5.8 | 4.6 | 4.0 | 
Spectroscopy Hi z Exp time | 5500 | 6780 | 10800 | 13300 | 
Shots/visit | 8 | 4 | 4 | 4 | 
Hours/visit | 12.2 | 7.5 | 12.0 | 14.7 | 
Lo z Exp time | 2500 | 2500 | 2500 | 2500 | 
Shots/visit | 16 | 20 | 16 | 12 | 
Hours/visit | 11.1 | 13.9 | 11.1 | 8.3 | 

## Slide 27: 2 Tier survey to z = 1.7 DRM 2 FoM = 238
Z No S/N No S/N Total σsta σ/√N σsys σtotal
0.15 8 11.49 2 26.50 11 0.107 0.031 0.006 0.031
0.25 26 5.38 8 12.41 35 0.114 0.019 0.007 0.020
0.35 52 3.26 17 7.52 69 0.124 0.015 0.008 0.017
0.45 87 2.37 29 5.47 116 0.130 0.012 0.008 0.014
0.55 127 1.81 42 4.18 170 0.137 0.011 0.009 0.014
0.65 169 1.39 56 3.20 225 0.146 0.010 0.009 0.013
0.75 210 1.04 70 2.39 280 0.157 0.009 0.010 0.014
0.85 0 0.81 86 1.86 86 0.142 0.015 0.010 0.018
0.95 0 0.77 99 1.77 99 0.148 0.015 0.011 0.018
1.05 0 0.74 110 1.72 110 0.151 0.014 0.011 0.018
1.15 0 0.70 115 1.61 115 0.157 0.015 0.012 0.019
1.25 0 0.67 115 1.55 115 0.162 0.015 0.012 0.020
1.35 0 0.63 112 1.45 112 0.168 0.016 0.013 0.021
1.45 0 0.55 104 1.28 104 0.172 0.017 0.014 0.022
1.55 0 0.50 93 1.15 93 0.176 0.018 0.014 0.023
1.65 0 0.45 82 1.04 82 0.185 0.020 0.015 0.025

## Slide 28: Supernova FoM Summary
Z max | DRM 1 | DRM 2
1.2 | 105 | 110
1.4 | 130 | 131
1.6 | 150 | 151
1.7 | 156 | 157
Z max | DRM 1 | DRM 2
1.2 | 171 | 183
1.4 | 207 | 208
1.6 | 231 | 233
1.7 | 235 | 238
Conservative
σsys = 0.02(1+z)/1.8
Optimistic
σsys = 0.01(1+z)/1.8

## Slide 29: Systematic Errors
The Figures of Merit depend sensitively on the systematic errors assumed. These errors depend on, among other things,
  Photometric calibrations over the large redshift range
  Corrections for the filter bands translating to different SNe rest frame bands (K corrections)
  Extinction corrections
  Malmquist bias effects etc
  Supernova evolution
We have simulated these errors and for the first round of calculations; are using σsys= 2%[(1+z)/1.8]
More work on this challenging issue is in progress, including correlated errors across the z bins, which may reduce (or increase??) this number

## Slide 30: Supernova with DRM 2 with an IFU spectrometer
Can think of three strategies to use an IFU:
1 .Use the Imager to discover the supernovae and get lightcurves in 3 filter bands and use the IFU Spectrometer to type the supernovae and measure redshifts, with similar S/N as the coadded slitless spectra. FoM=300 for Zmax=1.7
2. Use the Imager to discover the supernovae and get lightcurves in 3 filter bands and use the IFU Spectrometer to take a “Deep spectrum” to allow the use of spectral feature ratios to reduce intrinsic spread. FoM=221 for Zmax=1.6
3. Use the imager to discover the supernova, and use the IFU to type the SNe, get redshifts, and get the ligh tcurves from the spectra. FoM=212 for Zmax=1.4

## Slide 31: Supernova with DRM 2 with an IFU spectrometer
Do calculations with the first strategy
1.Use the Imager to discover the supernovae
and get lightcurves in 3 filter bands
2.Use the IFU Spectrometer to type the supernovae and measure redshifts, with
similar S/N as the coadded slitless spectra

## Slide 32: Survey Plan
6 month supernova survey
Spread over 1.8 years calendar time
Do supernovas with a 5 day cadence
1.8yrs = 657 days, 110 visits for SNe
Use 32 hours per visit
  131 visits x 33 hours/24 = 180 days = 0.5 years

## Slide 33: Exposure Time Calculations
For the imager exposure times, same as described above for the slitless survey
For the IFU, the input parameters used in exposure time estimates were
  1.1 m off axis telescope
  IFU spectrometer with an R = 50 (i.e.100/pixel)
  A single “selected best” NIR detector, run cooler, with
    plate scale = 0.26”/pix
    read noise = 5 e
    dark current = 0.01 e/pix/sec
    Wavelength reach up to 2.6 microns
  Used the time estimates from Alex Kim scaled to give a 5 σ detection of the Silicon line to identify SNe as Type 1a

## Slide 34: IFU Exposure Times from Alex Kim
<Z> Spectra 9 Spectra(d) Cumulative (days)
1 Visit(sec) 100 SNe Spect +slew time
0.15 12.71 0.13 0.13 0.46
0.25 34.22 0.36 0.49 1.14
0.35 68.16 0.71 1.20 2.17
0.45 115.93 1.21 2.41 3.70
0.55 179.06 1.87 4.27 5.89
0.65 259.44 2.70 6.97 8.92
0.75 359.30 3.74 10.72 12.99
0.85 481.86 5.02 15.74 18.33
0.95 630.40 6.57 22.30 25.22
1.05 808.41 8.42 30.72 33.96
1.15 1019.94 10.62 41.35 44.91
1.25 1269.59 13.22 54.57 58.46
1.35 1560.95 16.26 70.83 75.05
1.45 1898.81 19.78 90.61 95.15
1.55 2287.72 23.83 114.44 119.30
1.65 2732.49 28.46 142.91 148.09
Time for 100 supernova, 7 IFU spectra and 1 Reference spectrum, 1.1 m mirror
Exposure times to get S/N=15 in synthetic band for 12% meas errors on SNe peak mag
Times for spectra
Include time for
the Reference
Spectrum

## Slide 35: End Effects
Type 1a lightcurve has a two week rise to peak with a six week decline
Must get lightcurve as a minimum 10 days before peak and follow to 25 days past peak for a total follow up time of at least 35 days in the supernova rest frame. This translates into an observer frame time of
Z Observer fr days Discovery Time No of Visits
0.8 63 657-63=594 119
1.7 94 657-94=563 113
Thus the discovery scans are carried out for the first 594, or 563 days for the two redshift tiers ( out of 1.8 yrs = 657 days)

## Slide 36: Error Model Used
Used the program by Eric Linder used in the last round of SNAP Figure of Merit calculations
Statistical errors i.e. errors that are reduced by 1/sqrt(N)
  σintrinsic= (10 + 3.3z)% for the inherent spread
  12 % measurement errors per supernova
  Add these in quadrature and divide by sqrt N(z) to get σstat
Systematic error σsys = 0.02[1μ/(λ0/(1+z))] where λ0 is the center of the reddest band (2.4 for a 2.2 to 2.6 synthetic band) except for the first bin (z<0.1)
Add these in quadrature σtot = sqrt(σstat2 + σsys2)

## Slide 37: Survey Strategies
Mission | DRM1 | DRM2 | DRM2- IFU |  | 
Hi z(z<1.7) Imaging | 1.80 | 1.96 | 5.88 |  | 
Exp time | 1500 | 1800 | 1500 |  | 
Shots/visit | 5 x 3 | 4 x 3 | 12 x 3 |  | 
hours/visit | 6.25 | 6.0 | 15.0 |  | 
Lo z(z<0.8) Imaging | 6.48 | 5.88 | 9.8 |  | 
Exp time | 300 | 400 | 450 |  | 
Shots/visit | 18 x 3 | 12 x 3 | 20 x 3 |  | 
Hours/visit | 4.5 | 4.0 | 7.5 |  | 
Spectroscopy Hi z Exp time | 9500 | 13300 | variable |  | 
Shots/visit | 5 | 4 | No of SNe |  | 
Hours/visit | 13.2 | 14.7 | 8.0 |  | 
Lo z Exp time | 1800 | 2500 |  |  | 
Shots/visit | 18 | 12 |  |  | 
Hours/visit | 9.0 | 8.3 |  |  | 

## Slide 38: IFU Survey to z = 1.7 with DRM 2 FoM = 300
<Z> SNe S/N SNe S/N SNe σstat σ/√N σsys σtot
Low z Hi z Total
0.15 14 2.12 8 2.12 22 0.11 0.023 0.006 0.024
0.25 43 2.12 24 2.12 67 0.12 0.014 0.007 0.016
0.35 83 2.12 47 2.12 130 0.13 0.011 0.008 0.013
0.45 139 2.12 79 2.12 218 0.13 0.009 0.008 0.012
0.55 204 2.12 115 2.12 319 0.14 0.008 0.009 0.011
0.65 270 2.12 153 2.12 423 0.14 0.007 0.009 0.012
0.75 336 2.12 190 2.12 527 0.15 0.007 0.010 0.012
0.85 0 2.12 234 2.12 234 0.14 0.009 0.010 0.014
0.95 0 2.12 271 2.12 271 0.15 0.009 0.011 0.014
1.05 0 2.12 299 2.12 299 0.15 0.009 0.011 0.014
1.15 0 2.12 312 2.12 312 0.16 0.009 0.012 0.015
1.25 0 2.12 314 2.12 314 0.16 0.009 0.012 0.016
1.35 0 2.12 305 2.12 305 0.17 0.010 0.013 0.016
1.45 0 2.12 283 2.12 283 0.17 0.010 0.014 0.017
1.55 0 2.12 254 2.12 254 0.18 0.011 0.014 0.018
1.65 0 2.12 223 2.12 223 0.18 0.012 0.015 0.019
Systematic error = 0.01(1+z)/2.4

## Slide 39: Screening Candidates to identify Type 1a’s
Will need to screen 2 candidates to get 1 good Type 1a
In calculating the time required for IFU spectroscopy allow for two spectra for each of the total number of supernovae in each redshift bin on the previous table

## Slide 40: Supernova FoM Summary
Z max | DRM 1 | DRM 2 | DRM 2 IFU
1.2 | 105 | 110 | 120
1.4 | 130 | 131 | 147
1.6 | 150 | 151 | 169
1.7 | 156 | 157 | 179
Z max | DRM 1 | DRM 2 | DRM 2 IFU
1.2 | 171 | 183 | 214
1.4 | 207 | 208 | 257
1.6 | 231 | 233 | 287
1.7 | 235 | 238 | 300
Conservative
σsys = 0.02(1+z)/1.8
Optimistic
σsys = 0.01(1+z)/1.8

## Slide 41: Supernova with DRM 1
Slitless Spectroscopy 6 month survey
FoM with Planck prior only
FoM
Z max
Optimistic
Conservative

## Slide 42: Supernova with DRM 2 with IFU
Spectroscopy with IFU, 6 month Survey
FoM with Planck prior only
FoM
Z max
Conservative
Optimistic

## Slide 43: Supernova Surveys
Feature | ISWG | IDRM | DRM 1 | DRM 2 | DRM 2 IFU
Mirror Dia | 1.1 m | 1.3 m | 1.3 m | 1.1m | 1.1 m
Imager | 8 H2RG | 28 H2RG | 36 H2RG | 14 H4RG | 14 H4RG
Plate Scale | 0.45 “/pixl | 0.18 “/pixl | 0.18 “/pixl | 0.18 “/pixl | 0.18 “/pixl
Area | 0.5 sq deg | 0.28 sq deg | 0.36 sq deg | 0.56 sq deg | 0.56 sq deg
A(I)xA(T) | 0.48 | 0.37 | 0.48 | 0.53 | 0.53
SNe Spectro | IFU | Slitless | Slitless | Slitless | IFU
Lambda Max | 2.0 | 2.0 | 2.5 | 2.5 | 2.5
SNe Survey |  |  |  |  | 
Duration | 18 months | 6 months | 6 months | 6 months | 6 months
z max | 1.5 | 1.2 | 1.7 | 1.7 | 1.7
Tiers | 3 | 2 | 2 | 2 | 2
NO of SNe | 1698 | 1194 | 1798 | 1822 | 4201
FoM | 190 | 134 | 235 | 238 | 300

## Slide 44: FoM’s with Priors
Priors FoM
Planck+SNe 238
Planck+StageIII 116
Planck+StageIII+SNe 509
Planck+StageIII+BigBOSS+LSST 1103
Planck+StageIII+BigBOSS+LSST+SNe 1747
For Supernova (SNe) use WFIRST DRM 2 Slitless, z max = 1.7, with optimistic errors